# OmniBot Design Justification
## Electrical
### Component Selection
Where applicable, all components have been selected to conform with the Seeedstudio OPL for manufacturing and assembly.
### Decoupling
All decoupling capacitors are the standard values given in the STM32F10xx hardware design document.
### Programming/Debugging
Pin-outs were selected for the SWD interface based on the STLink/V2 and third party Tag-Connect connector and cable.
### Boot Mode
Jumper to select boot mode were selected due to cost and simplicity of use. 10K Resistors were selected from the STM32F10xx Hardware Design datasheet recommendations. BOOT0 has no further functionality, however BOOT1 can be used as a general I/O, so it is broken out to a further header bank.
### External Power Controller
Design was based off similar purpose IC chips linked below, capacitor (1nF) was estimated based on IC chip solutions. IC solution wasn't pursued as Seeedstudio did not have applicable parts in their OPL.
http://www.vishay.com/docs/73449/si1869dh.pdf
http://www.onsemi.com/pub_link/Collateral/AND9093-D.PDF
### Crystal
Crystal capacitance values were calculated using formulae derived from the following links.
Stray capacitance, from the STM32F103CBT6 datasheet lists the pin capacitance as 5pF. A further 2pF was estimated due to track considerations and a 20pF crystal was used for calculations regarding the High Speed External Clock.
http://www.seeedstudio.com/depot/images/opl/datasheet/306010033.pdf
http://ww1.microchip.com/downloads/en/AppNotes/00826a.pdf
Rs = 910ohms was calculated with the following link
http://www.crystek.com/documents/appnotes/Pierce-GateIntroduction.pdf
### USB
USB 2.0 High speed was selected over USB OTG primarily due to added cost of OTG with no added benefit for current application.